OPENFLAME BURNER		GROUP B-5 single jet.

......Spear Point Flame......				Range:      CD40

Pre-Mix.    Air-Gas.

Cat.		Type.		Thread			Kcal/Hr.

No.				  size	 	 	nominal

B051		CD40		3/8”    	bsp	  	10320

The Rapidflame policy is one of continuous development and improvement, we therefore reserve the right to change any specification or design without prior notice.

# Text boxes

# Introduction

The burner  is composed of a stainless steel nozzle and an aluminum body and designed for operating with a highly stable spearpoint shaped flame with a wide turn-down ratio, this burner nozzle offers excellent resistance when used in a corrosive environment or high temperature atmosphere. Pre-mixing with combustion air is complete with a fan, blower or compressed air supply to the venturi mixer. Mainly used with either Natural or Propane gas this type of nozzle provides an ideal assembly  when combined with the Rapidflame RAM and VM range of Venturi Mixers and control valves.

Applications

Flame Plasma surface treatment of plastic containers, cable and pipe prior to printing and coating. Edge melting and forming of glass tubing, plate and table ware.

Heating of wire and metal sections for heat treatment, forming and metal joining.